## Slide 1: Ultraflexible Smart FLoating Offshore Wind Turbine (USFLOWT)
https://arpa-e.energy.gov/?q=arpa-e-programs/atlantis
Model Linearization
David Stockhouse
Aoife Henry
Manuel Pusch
Oct. 8, 2021

## Slide 2: Overview
Inputs and Outputs
Excitation Signals
Model Error Metrics
Simulation Setup
Preliminary Results
Highlighted Issues

## Slide 3: Inputs and Outputs
Main Inputs (to be excited)
  horizontal wind (uniform)
  blade pitch (collective)
  generator torque
  cable tension (collective)
  etc.
Main Outputs (to be evaluated)
  generator speed
  generator power
  platform pitch
  tower base moment
  blade root bending moment
  drive train torque
  etc.
Notes: Other inputs: yaw angle, wave, wind shear, etc.

## Slide 4: Excitation Signals
Types
  step
  ramp
  sine
  sweep
  noise
Parametrization
  amplitude
  frequency / bandwidth

## Slide 5: Model Error Metrics
Time Domain
  maximum
  root mean square
  settling time
Frequency Domain (using FFT)
  maximum ( norm)
  root mean square ( norm)
  frequency weighting!
Other Aspects
  stability
  non-minimum phase behavior

## Slide 6: Simulation Setup
Open-loop (assuming open-loop stability)
  Without leaving proximity of operating point
  Frequency response comparison
    How accurate is the linear model for various frequencies/amplitudes?
Closed-loop
  Step disturbance
    Test difference of linear/nonlinear control response
    From how large a step can the system recover?
  Small-scale DLC

## Slide 7: Preliminary Results: Linear Model Analysis
Structure of Matrices
  state coupling
Model Order Reduction
  Minimum Realization
  Instability contribution
  MANUEL

## Slide 8: Preliminary Results: Comparison Linear / Nonlinear Model
plots comparing time series?
evaluation/visualization of some error metrics?

## Slide 9: Highlighted Issues
HydroDyn states, including wave input, in linear model?
Set (steady state) initial values for nonlinear simulation (OpenFAST)?
  problem with platform pitch angle
Linearized models have unstable poles