## Slide 1: Ultraflexible Smart FLoating Offshore Wind Turbine (USFLOWT)
https://arpa-e.energy.gov/?q=arpa-e-programs/atlantis
Model Linearization
David Stockhouse
Aoife Henry
Manuel Pusch
Dec. 3, 2021

## Slide 2: Model Linearization
inputs:
states:
outputs:
steady state operation point
applied deviation
nonlinear model
linear model

## Slide 3: Inputs and Outputs
Inputs ()
  collective blade pitch
  generator torque
Outputs ()
  rotor speed
  platform pitch
  platform heave
  platform surge
Wind Speeds (steady)
  m/s
  m/s
  m/s
Notes: Other inputs: yaw angle, wave, wind shear, etc.

## Slide 4: Inputs: Disturbance Signals
Types
  positive step
  negative step
  sine
Parametrization
  amplitude
  frequency
  Apply disturbance at
  Hold disturbance
  End simulation at
Notes: Will never reach steady-state for sine disturbance
Steady-state not that relevant, even then only for step
Metric = |y_nonlin – y_lin|, integral error
Goal: 2 responses should be as similar as possible after TDist

## Slide 5: Time Domain Outputs: Steady-State Error

## Slide 6: Simulation Setup
Recompile ROSCO controller to allow for open-loop control
Setup WEIS Python workflow to run on RC (Research Computing) resources.
Perform MBC transform on .lin files
Generate disturbance cases for range of amplitudes/frequencies
Set nonlinear initial conditions to linear operating points and run system for all cases.
Run linear system for all cases
Measure over range of step amplitudes (in case of step disturbance) and critical frequencies (in case of sinusoidal disturbance).
Find maximum disturbance step amplitude for which linear system significantly deviates from nonlinear system
Perform inverse MBC transform to analyze rotating states

## Slide 7: Highlighted Issues & Open Questions
Applying the disturbance signal and ending simulation as soon as the system has reached steady-state is currently not possible in WEIS, and linear system solve method is unreliable => recommend transferring linearization testing workflow to Simulink.
Difficulties utilizing ‘CalcSteady’ feature – system does not converge.
Lack of initial-value options in input files other than ElastoDyn.
How best to quantify steady-state? – moving-average filter over some , some threshold for each quantity ? => Manuel
Ambiguity on which quantities to use for initial conditions for blade-pitch vs. => mbc transform or not, stick to ctrl inputs
Suggestions on step amplitudes, sine frequencies, disturbance signals, output metrics etc to test?

## Slide 8
BACKUP